## Slide 1: arduino upgrade

## Slide 2
API
Port 7500
Node 0
Arduino node
4 Actuator & 4 Sensors
Actuator
target
report
NOW
Check whether the computer has sent any new serial commands.
Read the sensors and control the motor every 100 ms.
Send status data to Python every 1000 ms.
const int DEFAULT_TARGET = 50;
const int TARGET_DEADBAND = 10;
const int DRIVE_PWM = 70;
const int MEDIAN_SAMPLES = 7;
const unsigned long SAMPLE_INTERVAL_MS = 100;
const unsigned long TELEMETRY_INTERVAL_MS = 1000;
Closed-loop control is mainly achieved using a lower motion speed and a wider deadband.

## Slide 3: Limitations of the current control method:
Using a low speed and a large deadband can achieve closed-loop control and prevent oscillation, but it increases the motion completion time and provides insufficient positioning accuracy. A PID control algorithm could be added to improve the system.
Automatically executing a motion to a target position of 50 immediately after power-up may present a safety risk. It is recommended that this motion be performed only after an initialization command is received.
The relationship between the cable-pull sensor output and the actual length needs to be recalibrated to ensure that it is linear and accurate.

## Slide 4: PID
Proportional term (P) responds to the current error. The larger the difference between the target and the current position, the stronger the control output. It helps the actuator move quickly toward the target.
Integral term (I) responds to accumulated error over time. It is used to eliminate small remaining errors that the proportional term alone cannot remove. However, if it is too large, it can cause overshoot or oscillation.
Derivative term (D) responds to how quickly the error is changing. It helps the system slow down when the actuator is approaching the target too quickly, reducing overshoot and improving stability.

## Slide 5
API
Port 7500
Node 0
Arduino node
4 Actuator & 4 Sensors
Actuator
target
report
Add a PID controller
Check whether the computer has sent any new serial commands.
Read the sensors and control the motor every 100 ms.
Send status data to Python every 1000 ms.
Step 2: Add Proportional(P) control—the farther the actuator is from the target position, the faster it moves.
const int PWM_MIN = 60;
const int PWM_MAX = ???;
const float KP = 0.45;
int pwm = PWM_MIN + (int)(KP * absoluteError)
Step 1: Determine the maximum and minimum PWM values that can be reliably applied.
The proportional gain (P value) needs to be determined through testing.
Step 3: Add Derivative (D) control. When the actuator approaches the target rapidly, reduce the drive effort in advance to prevent overshoot.
Derivative (D) control is sensitive to sensor noise. The existing hardware filtering and software noise-reduction algorithms should be sufficient to meet the requirements.

## Slide 6
API
Port 7500
Node 0
Arduino node
4 Actuator & 4 Sensors
Actuator
target
report
Add a PID controller
Check whether the computer has sent any new serial commands.
Read the sensors and control the motor every 100 ms.
Send status data to Python every 1000 ms.
Step 4: Add integral (I) control, mainly to eliminate accumulated error and improve the final positioning accuracy.
Integral control may not be necessary.
It can also easily cause oscillation.
If the test results meet the required accuracy, it can be omitted.